## Slide 1
Column Pressure = Feed Pressure
Feed
Saturated Liquid
Temperature = 30 °C
Flow rate = 3000 kgmol/hr
Alkane | Mol fraction
Propane | 0.1
i-Butane | 0.05
i-Pentane | 0.36
n-Hexane | 0.4
n-Heptane | 0.09
Distillate
C6 = 0.01 (mol fraction)
Bottoms
C5 = 0.01 (mol fraction)
Find
Minimum reflux ratio
Minimum number of stages
Actual number of stages
Feed stage location